## Slide 1: Yield Analysis of Nano-Crossbar Arrays For Uniform and Clustered Defect Distributions
Emerging Circuits and Computation Group (ECC)
www.ecc.itu.edu.tr
Onur Tunali 1 and Mustafa Altun 2
onur.tunali@itu.edu.tr and altunmus@itu.edu.tr
Nanoscience and Nanoengineering Department (1) and Electronics and Communications Department (2)
Istanbul Technical University
ICECS 17 IEEE International Conference on Electronics, Circuits and Systems
5-8 December, Batumi - Georgia
This work is part of a project that has received funding from the European Union's H2020 research and innovation programme under the Marie Skłodowska-Curie grant agreement No 691178.
This work is supported by the TUBITAK-Career project #113E760

## Slide 2: Outline
Nano-crossbars arrays (Reconfigurable)
Logic mapping of nano-crossbar arrays
Main problem and previous works
Yield in the context of crossbars (Area Size)
Probability of successful logic mapping
Yield formalization for uniform defects
Clustered defect distribution
Regional analysis of defects
Experimental results
Conclusion

## Slide 3: Nano-crossbar Arrays
[1]
__________________________________
[1] H. Yan, H. S. Choe, S. Nam, Y. Hu, S. Das, J. F. Klemic, J. C. Ellenbogen, and C. M. Lieber, “Programmable nanowire circuits for nanoprocessors,” Nature
Cross section of an activated switch
Switching Element
Very similar to Programmable Logic Arrays (PLA)
[1]

## Slide 4: Logic Mapping of Nano-crossbar
O1
O2
O3
O4
Defective crossbar
I1 I2 I3 I4 I5 I6
: Configurable Switch
: Defective Switch
f = x1 x2 + x1 x3 + x2 x3 + x1 x2 x3
Given logic function
Assignment and configuration
P1
P2
P4 P3
x2 x3 x1 x1 x2 x3
: Activated Switch
: Deactivated Switch
Mapping
Algorithm

## Slide 5: Logic Mapping of Nano-crossbar
O1
O2
O3
O4
I1 I2 I3 I4 I5 I6
: Configurable Switch
: Defective Switch
f = x1 x2 + x1 x3 + x2 x3 + x1 x2 x3
Given logic function
NO MAPPING!
Too many defects

## Slide 6: Main Problem and Previous Works
How can we predict sufficient area size of crossbar ensuring a successful mapping of a given logic function independent of defect distributions ?
  We formalize the yield and probability of successful logic mapping of a crossbar in terms of area overheads.
  Then, we minimize area overhead while maximizing the mapping probability.

## Slide 7: Main Problem and Previous works
The most of previous works use 1.5 times larger crossbars for logic mapping disregarding the yield. Another tendency is to consider only uniform defect distributions. In addition, certain studies use random logic functions.
  We cover both uniform and clustered distributions.
  We show that 1.5 times area overheads are too generous.
  And, we show that random logic functions are not suitable to obtain reliable results.

## Slide 8: Yield in the context of crossbars
1. Step : Formulation of optimal area size
Inputs of crossbar
(N)
6 literals ( x1, x2 , x3 , x1, x2, x3)
f = x1 x2 + x1 x3 + x2 x3 + x1 x2 x3
P1
P2
P4 P3
x2 x3 x1 x1 x2 x3
Optimal Area = # of products x # of literals
Size = M x N
Area Cost = 4 x 6 = 24
Outputs of crossbar
(M)
4 Products ( P1, P2 , P3, P4 )

## Slide 9: Yield in the context of crossbars
P1
P2
P4 P3
x2 x3 x1 x1 x2 x3
2. Step : Formulation of area size with overheads
Area size with = (M.k0) x ( N.ki )
overheads
Area Cost = 6 x 9 = 63
ki : Input overhead coefficient
How large input size
(N. ki)
How large output size
(M. k0)
k0 : Output overhead coefficient

## Slide 10: Yield in the context of crossbars
3. Step : Formulation of yield
Yield =
Yield
Yield only related area overhead coefficients
Maximizing yield means less area cost

## Slide 11: Probability of Successful Mapping
Probability of successful logic mapping with uniform defects
Number of products denoted with M
Increasing diminish defect rate
Increasing raise outputs
: Logic inclusion ratio of
ith product
: Optimal area size
: Input coefficient
: Output coefficient
: Defect Rate

## Slide 12: Yield Formalization for Uniform Defects
Maximizing yield means finding minimum area coefficients making Psuc = 1
Since yield is only dependent on area coefficients, given constraints ensures a maximum yield
Knowing only logic function and defect rate we predict sufficient area size for successful logic mapping
Yield

## Slide 13: Clustered Defect Distribution
Since “cluster is in the eye of beholder”, it is hard to formulate and different regions have different defect rates. Also, we don’t have enough field data.
Defect rate is 20%: (a) – (b) denser to looser clustering patterns (c) uniform distribution (d) literal distribution and (e) – (f) sorted uniform and clustered distributions

## Slide 14: Regional Analysis of Defects
Defect distributions are sorted. Then, regional densities are found and charted for comparison
: # of defective switches ith region
: Density of ith region
A0
A1
A2

## Slide 15: Regional Analysis of Defects
Comparison of regional densities of uniform and clustered distributions gives us which uniform defect rate (Pd) to use in yield analysis
Chart: Sub Regions
| 0 | 3 | 5 | 7 | 10 | 13 | 15
Uni. Dist. (Pd=20%) | 0.35 | 0.32 | 0.27 | 0.24 | 0.1 | 0.1 | 0.08
Uni. Dist. (Pd=25%) | 0.4 | 0.35 | 0.28 | 0.26 | 0.15 | 0.12 | 0.09
Uni. Dist. (Pd=30%) | 0.5 | 0.37 | 0.35 | 0.29 | 0.17 | 0.13 | 0.1
Clus. Dist. (Pd=20%) | 0.47 | 0.27 | 0.24 | 0.15 | 0.05 | 0.02 | 0.01
Pd = 30% All region densities are larger than clustered distributions

## Slide 16: Literal Distributions
Literal distribution shows the crossbar representation of a logic function. Using a matrix is a common choice. Activated switches are shown with 1s.
P1
P2
P3 P4
x1 x2 x3 x1 x2 x3
f = x1 x2 + x1 x3 + x2 x3 + x1 x2 x3
x1 x2 x3 x1 x2 x3
P1
P2
P3 P4

## Slide 17: Literal Distributions
Due to logic function properties, a product cannot have a variable and its negation at the same time. So there are 2 constraints literal distributions need to adhere:
We will show that randomly generated logic function matrices produce unreliable results.
  At most, only half of a matrix row can be 1
x1 x2 x3 x1 x2 x3
P1
P1 = x1 x2 x3 x1
invalid
x1 x2 x3 x1 x2 x3
P1
P1 = x2 x3 x2
invalid
  If an element corresponding to a variable is 1, the element corresponding to its negation must be zero.

## Slide 18: Experimental Results Random Functions
Bench |  | ko - ki = 1 - 1 |  | ko - ki = 1.1 - 1.1 |  | ko - ki = 1.2 - 1 |  | ko - ki = 1 - 1.2 | 
No | IR | Uni | Clu | Uni | Clu | Uni | Clu | Uni | Clu
1* 2 | 40% 40% | 0% 0% | 0% 0% | 0% 4% | 0% 0% | 0% 16% | 0% 0% | 0% 10% | 0% 0%
3* 4 | 35% 35% | 0% 4% | 0% 0% | 0% 100% | 0% 0% | 100% 100% | 8% 8% | 100% 100% | 2% 10%
5* 6 | 30% 30% | 100% 100% | 0% 0% | 100% 100% | 64% 64% | 100% 100% | 90% 75% | 100% 100% | 84% 76%
7* 8 | 25% 25% | 100% 100% | 6% 16% | 100% 100% | 98% 100% | 100% 100% | 98% 100% | 100% 100% | 98% 100%
* generated according to the logic function constraints
ko : Output coefficient ki : Input coefficient IR : Logic inclusion ratio Uni : Uniform Clu : Clustered
Success Rates wıth Dıfferent Yıeld Values Regardıng Random Benchmarks
Defect Rate Pd = 20%
Bench |  | ko - ki = 1 - 1 |  | ko - ki = 1.1 - 1.1 |  | ko - ki = 1.2 - 1 |  | ko - ki = 1 - 1.2 | 
No | IR | Uni | Clu | Uni | Clu | Uni | Clu | Uni | Clu
1* 2 | 40% 40% | 0% 0% | 0% 0% | 0% 4% | 0% 0% | 0% 16% | 0% 0% | 0% 10% | 0% 0%
3* 4 | 35% 35% | 0% 4% | 0% 0% | 0% 100% | 0% 0% | 100% 100% | 8% 8% | 100% 100% | 2% 10%
5* 6 | 30% 30% | 100% 100% | 0% 0% | 100% 100% | 64% 64% | 100% 100% | 90% 75% | 100% 100% | 84% 76%
7* 8 | 25% 25% | 100% 100% | 6% 16% | 100% 100% | 98% 100% | 100% 100% | 98% 100% | 100% 100% | 98% 100%

## Slide 19: Experimental Results Benchmarks
Success Rate of Tunali’s Algorıthm (Best Runtıme – Reasonable Success rate)
wıth Proposed and 1.5 Times Area Overheads
Pd = 20%
Benchmarks |  |  | Tunali [9] |  |  |  |  |  |  |  |  | 
 |  |  | Optimum |  | Proposed |  |  |  |  |  | ko - ki = 1.5-1.5 | 
Name | Size | IR | Uni | Clu | Uni | ko | ki | Clu | ko | ki | Uni | Clu
xor5 | 16 × 10 | 50% | 76% | 16% | 100% | 1.4 | 1.4 | 100% | 1.6 | 1.6 | 100% | 100%
squar5 | 32 × 10 | 50% | 12% | 0% | 100% | 1.5 | 1 | 100% | 1.8 | 1 | 100% | 100%
bw | 87 × 10 | 40% | 60% | 10% | 100% | 1.2 | 1 | 100% | 1.2 | 1 | 100% | 100%
ex5p | 256 × 16 | 50% | 0% | 0% | 100% | 1.3 | 1 | 100% | 1.5 | 1 | 100% | 100%
apex4 | 438 × 18 | 46% | 0% | 0% | 100% | 1.2 | 1 | 100% | 1.3 | 1 | 100% | 100%
sao2 | 58 × 20 | 36% | 0% | 0% | 100% | 1.5 | 1 | 100% | 1.5 | 1.4 | 100% | 100%
table3 | 175 × 28 | 41% | 0% | 0% | 100% | 1.4 | 1 | 100% | 1.4 | 1 | 100% | 100%
t481 | 481 × 32 | 31% | 0% | 0% | 100% | 1.2 | 1 | 100% | 1.2 | 1.1 | 100% | 100%
table5 | 158 × 34 | 35% | 0% | 0% | 94% | 1.3 | 1.2 | 100% | 1.6 | 1.5 | 100% | 100%
duke2 | 87 × 44 | 20% | 0% | 32% | 100% | 1.3 | 1.2 | 100% | 1.6 | 1.5 | 100% | 100%
apex1 | 206 × 90 | 10% | 0% | 58% | 100% | 1.2 | 1 | 100% | 1.4 | 1.3 | 100% | 100%
apex3 | 280 × 108 | 8% | 0% | 40% | 100% | 1.2 | 1 | 100% | 1.2 | 1.2 | 100% | 100%
Benchmarks |  |  | Tunali [9] |  |  |  |  |  |  |  |  | 
 |  |  | Optimum |  | Proposed |  |  |  |  |  | ko - ki = 1.5-1.5 | 
Name | Size | IR | Uni | Clu | Uni | ko | ki | Clu | ko | ki | Uni | Clu
xor5 | 16 × 10 | 50% | 76% | 16% | 100% | 1.4 | 1.4 | 100% | 1.6 | 1.6 | 100% | 100%
squar5 | 32 × 10 | 50% | 12% | 0% | 100% | 1.5 | 1 | 100% | 1.8 | 1 | 100% | 100%
bw | 87 × 10 | 40% | 60% | 10% | 100% | 1.2 | 1 | 100% | 1.2 | 1 | 100% | 100%
ex5p | 256 × 16 | 50% | 0% | 0% | 100% | 1.3 | 1 | 100% | 1.5 | 1 | 100% | 100%
apex4 | 438 × 18 | 46% | 0% | 0% | 100% | 1.2 | 1 | 100% | 1.3 | 1 | 100% | 100%
sao2 | 58 × 20 | 36% | 0% | 0% | 100% | 1.5 | 1 | 100% | 1.5 | 1.4 | 100% | 100%
table3 | 175 × 28 | 41% | 0% | 0% | 100% | 1.4 | 1 | 100% | 1.4 | 1 | 100% | 100%
t481 | 481 × 32 | 31% | 0% | 0% | 100% | 1.2 | 1 | 100% | 1.2 | 1.1 | 100% | 100%
table5 | 158 × 34 | 35% | 0% | 0% | 94% | 1.3 | 1.2 | 100% | 1.6 | 1.5 | 100% | 100%
duke2 | 87 × 44 | 20% | 0% | 32% | 100% | 1.3 | 1.2 | 100% | 1.6 | 1.5 | 100% | 100%
apex1 | 206 × 90 | 10% | 0% | 58% | 100% | 1.2 | 1 | 100% | 1.4 | 1.3 | 100% | 100%
apex3 | 280 × 108 | 8% | 0% | 40% | 100% | 1.2 | 1 | 100% | 1.2 | 1.2 | 100% | 100%

## Slide 20: Experimental Results Benchmarks
Success Rate of Yuan’s Algorıthm (Reasonable Runtıme – Best Success rate)
wıth Proposed and 1.5 Times Area Overheads
Pd = 20%
Benchmarks |  |  | Yuan [10] |  |  |  |  |  |  |  |  | 
 |  |  | Optimum |  | Proposed |  |  |  |  |  | ko; ki = 1:5; 1:5 | 
Name | Size | IR | Uni | Clu | Uni | ko | ki | Clu | ko | ki | Uni | Clu
xor5 | 16 × 10 | 50% | 78% | 12% | 100% | 1.4 | 1.4 | 100% | 1.6 | 1.6 | 100% | 100%
squar5 | 32 × 10 | 50% | 14% | 0% | 100% | 1.5 | 1 | 100% | 1.8 | 1 | 100% | 100%
bw | 87 × 10 | 40% | 60% | 14% | 100% | 1.2 | 1 | 100% | 1.2 | 1 | 100% | 100%
ex5p | 256 × 16 | 50% | 0% | 0% | 100% | 1.3 | 1 | 100% | 1.5 | 1 | 100% | 100%
apex4 | 438 × 18 | 46% | 0% | 0% | 100% | 1.2 | 1 | 100% | 1.3 | 1 | 100% | 100%
sao2 | 58 × 20 | 36% | 0% | 0% | 100% | 1.5 | 1 | 100% | 1.5 | 1.4 | 100% | 100%
table3 | 175 × 28 | 41% | 0% | 0% | 100% | 1.4 | 1 | 100% | 1.4 | 1 | 100% | 100%
t481 | 481 × 32 | 31% | 0% | 0% | 100% | 1.2 | 1 | 100% | 1.2 | 1.1 | 100% | 100%
table5 | 158 × 34 | 35% | 0% | 0% | 100% | 1.3 | 1.2 | 100% | 1.6 | 1.5 | 100% | 100%
duke2 | 87 × 44 | 20% | 0% | 50% | 100% | 1.3 | 1.2 | 100% | 1.6 | 1.5 | 100% | 100%
apex1 | 206 × 90 | 10% | 0% | 70% | 100% | 1.2 | 1 | 100% | 1.4 | 1.3 | 100% | 100%
apex3 | 280 × 108 | 8% | 0% | 86% | 100% | 1.2 | 1 | 100% | 1.2 | 1.2 | 100% | 100%
Benchmarks |  |  | Yuan [10] |  |  |  |  |  |  |  |  | 
 |  |  | Optimum |  | Proposed |  |  |  |  |  | ko; ki = 1:5; 1:5 | 
Name | Size | IR | Uni | Clu | Uni | ko | ki | Clu | ko | ki | Uni | Clu
xor5 | 16 × 10 | 50% | 78% | 12% | 100% | 1.4 | 1.4 | 100% | 1.6 | 1.6 | 100% | 100%
squar5 | 32 × 10 | 50% | 14% | 0% | 100% | 1.5 | 1 | 100% | 1.8 | 1 | 100% | 100%
bw | 87 × 10 | 40% | 60% | 14% | 100% | 1.2 | 1 | 100% | 1.2 | 1 | 100% | 100%
ex5p | 256 × 16 | 50% | 0% | 0% | 100% | 1.3 | 1 | 100% | 1.5 | 1 | 100% | 100%
apex4 | 438 × 18 | 46% | 0% | 0% | 100% | 1.2 | 1 | 100% | 1.3 | 1 | 100% | 100%
sao2 | 58 × 20 | 36% | 0% | 0% | 100% | 1.5 | 1 | 100% | 1.5 | 1.4 | 100% | 100%
table3 | 175 × 28 | 41% | 0% | 0% | 100% | 1.4 | 1 | 100% | 1.4 | 1 | 100% | 100%
t481 | 481 × 32 | 31% | 0% | 0% | 100% | 1.2 | 1 | 100% | 1.2 | 1.1 | 100% | 100%
table5 | 158 × 34 | 35% | 0% | 0% | 100% | 1.3 | 1.2 | 100% | 1.6 | 1.5 | 100% | 100%
duke2 | 87 × 44 | 20% | 0% | 50% | 100% | 1.3 | 1.2 | 100% | 1.6 | 1.5 | 100% | 100%
apex1 | 206 × 90 | 10% | 0% | 70% | 100% | 1.2 | 1 | 100% | 1.4 | 1.3 | 100% | 100%
apex3 | 280 × 108 | 8% | 0% | 86% | 100% | 1.2 | 1 | 100% | 1.2 | 1.2 | 100% | 100%

## Slide 21: Conclusion
As a conclusion our contributions are as follows:
  We cover both uniform and clustered defect distributions
  We introduce an approximate formalization for an optimized yield considering uniform distributions;
  We propose a method to examine defect distributions by dividing crossbars into sub regions;
  By comparing uniform and clustered defects, we formulate a loose upper bound for yield considering clustered distributions;
  We show that our method is adaptive to changing parameters of logic functions and nano-crossbars.

## Slide 22: Thank You For Listening
QUESTIONS ?