## Slide 1: Nano-Crossbar based Computing: Lessons Learned and Future Directions
Design, Automation, and Test in Europe (DATE) , Grenoble France
March 10th, 2020
Presenter: Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/
This project has received funding from the European Union's H2020 research and innovation programme under the Marie Skłodowska-Curie grant agreement No 691178.
This work is supported by the TUBITAK-2501 project #218E068.
Mustafa Altun, Ismail Cevik, Ahmet Erten, Osman Eksik, Mircea Stan, and Csaba Andras Moritz

## Slide 2: Outline
Project Details
H2020 Rise Program
  Experiences in implementation
  Lessons learned
Project Summary in Numbers
Project’s Technical Contribution
  Computing with nano crossbars
  Lessons learned
  Future directions

## Slide 3: Project Details
title: | Synthesis and Performance Optimization of a Switching Nano-Crossbar Computer - NANOxCOMP
coordinator: | Mustafa Altun, ECC Group, Istanbul Technical University
partner(s): | Dr. Dan Alexandrescu, IROC Techonogies, France Prof. Lorena Anghel, TIMA Lab., France (partnership terminated) Prof. Valentina Ciriani, ALOS Lab., University of Milan, Italy. Prof. Csaba A. Moritz, Nanoscale Computing Fabrics Lab., University of Massachusetts, USA Prof. Kaushik Roy, Nanoelectronics Research Lab., Purdue University, USA Prof. Georgios Sirakoulis, Department of Electrical and Computer Engineering, Democritus University of Thrace, Greece (new partner) Prof. Mircea Stan, High-Performance Low-Power Lab., University of Virginia, USA Prof. Mehdi B. Tahoori, Dependable Nano-Computing Group, Karlsruhe Institute of Technology, Germany
funding agency & program: | European Union/European Commission H2020 MSCA Research and Innovation Staff Exchange Program (RISE)
Budget & duration: | 724.500 EURO & 2015-2019

## Slide 4: Project Details
Gathers globally leading research groups working on nanoelectronics and EDA
Focusing on computing with nano-crossbar arrays
Targets variety of nano crossbar based emerging technologies including nanowire/nanotube crossbar arrays, magnetic switch-based structures, and crossbar memories
Contributes to the construction of emerging computers beyond CMOS by proposing nano-crossbar based computer architectures.

## Slide 5: Specifics of MCSA RISE
Evaluation is mostly based on research excellence
  Propose with a good research idea
Money only for secondments/exchanges: 4500EURO per month
  4500 for the seconded researcher per month; at least 2000 for the researcher
  No secondment no Money!
  Seconded researchers should be employees in the sending organization
Cooperation between partners is the crucial part of RISE.
  Find good and attractive partners
  Large consortium is a plus
Although RISE is constructed on exchanges, you are expected to conduct productive research with publications/patents
  Have another project to support RISE
    Need funded researchers/scholars to work hard throughout the duration of the RISE project
    Need extra research money especially for experimental works

## Slide 6: Lessons Learned
PREPERATION
  Formation of the consortium
    Decision: industry partner or third country
    Faced Problem: only SME’s are eligible as industry partners
    Faced Problem: 2000EURO per month is not satisfactory for industry employees
    Faced Problem: limited budget makes hard to find partners
IMPLEMENTATION
  Difficulty of finding researchers to send
    Have an other project covering different research areas
    Have a sizable research group
  Difficulty of keeping the harmony between partners
    Joint papers, conference presentations, visits

## Slide 7: Lessons Learned
BENEFITS
  Building a network for long lasting collaborations
  Good for career developments of secondees, international experience
  Quality research with publications if not much Money needed
  Invaluable experience in implementing a project with a consortium having many partners
  Networking for future projects

## Slide 8: Project Summary in Numbers
Started in 2015, the project has been successfully completed in 2019 with achievements including:
34 researchers have been seconded to project partners, performing a total of 110,43 secondment months.
  17 of them are early stage researchers
  9 of them are female researchers.
32 peer-reviewed papers contributed by 30 project secondees or partners.
  12 of them are journal papers.
35 dissemination, outreach, and management activities have been performed.

## Slide 9: Research Motivation
MAIN GOAL: Showing efficient ways of computing with nano-crossbar arrays
WHY CROSSBAR ARRAYS?
REGULAR AND DENSE – AREA EFFICIENT
EASY TO MANIFACTURE
GOOD FOR RECONFIGURABILITY
Memory Structure
How about logic/computing in ASIC?

## Slide 10: Research Motivation
How about logic/computing in ASIC?
Same logic function implementations with conventional CMOS and crossbar based CMOS

## Slide 11: Research Progress
MAIN GOAL: Showing efficient ways of computing with nano-crossbar arrays

## Slide 12: Two-terminal vs. Four-terminal

## Slide 13: Two-terminal vs. Four-terminal
Shannon’s work: A Symbolic Analysis of Relay and Switching Circuits(1938)

## Slide 14: Two-terminal vs. Four-terminal
What are the Boolean functions implemented in (a) ad (b)?

## Slide 15: Research Progress: Logic Synthesis
MAIN GOAL: Showing efficient ways of computing with nano-crossbar arrays

## Slide 16: Diode/Memristor-based Model

## Slide 17: Diode/Memristor-based Model
Example:
Implement the Boolean function f = A+B with diode based nanoarrays.
Diode-resistor logic

## Slide 18: Diode/Memristor-based Model
Example:
Implement the Boolean function f = A B with diode based nanoarrays.
Diode-resistor logic

## Slide 19: Diode/Memristor-based Model
Example:
Implement the Boolean function f = A B + C D with diode based nanoarrays.

## Slide 20: FET-based Model
From Snider, G., et al., (2004). CMOS-like logic in defective, nanoscale crossbars. Nanotechnology.

## Slide 21: FET-based Model
Example:
Implement the Boolean function f = Aꞌ with FET based nanoarrays using CMOS-like logic.

## Slide 22: FET-based Model
Example:
Implement the Boolean function f = (A B + C D)ꞌ with FET based nanoarrays using CMOS-like logic.

## Slide 23: Four-terminal Switch-based Model
3 × 3 2D switching network and its lattice form

## Slide 24: Four-terminal Switch-based Model
Switches are controlled by Boolean literals.
fL evaluates to 1 iff there exists a top-to-bottom path.
gL evaluates to 1 iff there exists a left-to-right path.

## Slide 25: Four-terminal Switch-based Model
f3x3 = x1x4x7 + x2x5x8 +x3x6x9 +x1x4x5x8 +x2x5x4x7 +x2x5x6x9 +x3x6x5x8 +x1x4x5x6x9 +x3x6x5x4x7
Realizations of

## Slide 26: Experimental Results
Implementation of fXOR2 with different nanocrossbar types

## Slide 27: Experimental Results

## Slide 28: Research Progress: Fault Tolerance
MAIN GOAL: Showing efficient ways of computing with nano-crossbar arrays

## Slide 29: Defect/Fault Tolerance for FET/Diode/Memristor based Arrays
Permanent Faults occur mostly in fabrication and are tolerated in post-fabrication by redundancy and reconfigurability (mapping).
Transient Faults occur in field and are tolerated by redundancy

## Slide 30: Defect/Fault Tolerance for FET/Diode/Memristor based Arrays
O1
O2
O3
O4
Defective crossbar
I1 I2 I3 I4 I5 I6
: Configurable Switch
: Defective Switch
f = x1 x2 + x1 x3 + x2 x3 + x1 x2 x3
Given logic function
Assignment and configuration
P1
P2
P4 P3
x2 x3 x1 x1 x2 x3
: Activated Switch
: Deactivated Switch
Mapping
Algorithm
Defect tolerance is achieved by realizing a target logic function on a defective crossbar using row and column permutations
For the worst-case, N!M! permutations are required to find a successful mapping for NXM crossbar.

## Slide 31: Defect/Fault Tolerance for Four-Terminal Switch based Arrays
Lattice design
Sensitivity maps
Realize a target logic function on a sensitive crossbar such that total sensitivity is minimized thanks to redundant paths in lattices.

## Slide 32: Research Progress: RC Modelling
MAIN GOAL: Showing efficient ways of computing with nano-crossbar arrays

## Slide 33: RC Modelling
POST CMOS TECHNOLOGIES

## Slide 34: Research Progress: Technology Development
MAIN GOAL: Showing efficient ways of computing with nano-crossbar arrays

## Slide 35: Technology Development for Four-Terminal Switch based Arrays
How about the technology?
CMOS Implementation of Switching Lattices

## Slide 36: Technology Development for Four-Terminal Switch based Arrays
CMOS Implementation of Switching Lattices
Drain/Source contact-free (Metal-free) layouts!

## Slide 37: Technology Development for Four-Terminal Switch based Arrays
Circuit Structures

## Slide 38: Technology Development for Four-Terminal Switch based Arrays
EXPERIMENTAL RESULTS
Same logic function with conventional CMOS and crossbar based 65nm CMOS
In average 2X area improvement

## Slide 39: Technology Development for Four-Terminal Switch based Arrays
EXPERIMENTAL RESULTS
Post layout results on logic functions show that switching lattices occupy much smaller area than those of the conventional CMOS implementations, while they have competitive delay and power consumption values

## Slide 40
THANK YOU!
Web: http://www.nanoxcomp.itu.edu.tr/
PARTNERS
SECONDEES