## Slide 1: Integrated Synthesis Methodology for Crossbar Arrays
M. Ceylan Morgul, Luca Frontini, Onur Tunali, Elena Ioana Vatajelu,
Valentina Ciriani, Lorena Anghel, Csaba Andras Moritz, Mircea R. Stan,
Dan Alexandrescu, Mustafa Altun
This project has received funding from the European Union's H2020 research and innovation programme under the Marie Skłodowska-Curie grant agreement No 691178.
This work is supported by the TUBITAK-Career project #113E760

## Slide 2: Outline
Introduction
Proposed Integration Methodology
Logic Synthesis
Defect/Fault Tolerance
Conclusions

## Slide 3: Introduction
Nano-crossbars are emerged as an alternative to CMOS technology
  Cheap bottom-top nano-fabrication techniques
  Fabrics yield to be regular and dense
  Area and power efficient
  Easy to implement Boolean functions

## Slide 4: Introduction
Switching Nano-arrays
Switching nano array
Two-terminal switch
Four-terminal switch

## Slide 5: Introduction
Diode based
Memristor based
Switching Nano-arrays
Switching nano array
Two-terminal switch
Four-terminal switch
Notes: controlled by the voltage difference between the terminals.

## Slide 6: Introduction
Diode based
Memristor based
Switching Nano-arrays
FET based
Four-terminal
Switching nano array
Two-terminal switch
Four-terminal switch
Notes: FET based switch; here, the red line represents the controlling input. This is a unique opportunity that allows us to integrate well developed conventional circuit design techniques into nano-crossbar arrays
A four-terminal switch is given The controlling input, has a separate physical formation from the crossbar

## Slide 7: Introduction

## Slide 8: Introduction
Nanowire four-terminal switch
Spin-wave switch

## Slide 9: Outline
Introduction
Proposed Integration Methodology
Logic Synthesis
Defect/Fault Tolerance
Conclusions

## Slide 10: Integration Methodology
Permanent Defect Tolerance
Testing Transient Fault Tolerance Performance
Transient Fault
Tolerance
Performance Optimization
Fabrication
Logic Synthesis

## Slide 11: Outline
Introduction
Proposed Integration Methodology
Logic Synthesis
Defect/Fault Tolerance
Conclusions

## Slide 12: Logic Synthesis
Permanent Defect Tolerance
Testing Transient Fault Tolerance Performance
Transient Fault
Tolerance
Performance Optimization
Fabrication
Logic Synthesis

## Slide 13: Logic Synthesis
Crossbar size limits (area) and Function size
Fabrication Complexity
Function output number (Multi or single output realization)
Power and Delay Specifications
Application specification (memory based etc.)

## Slide 14: Introduction

## Slide 15: Introduction

## Slide 16: Introduction

## Slide 17: Introduction

## Slide 18: Introduction

## Slide 19: Introduction

## Slide 20: Logic Synthesis
Implementation of fXOR2 with different nanocrossbar types

## Slide 21: Outline
Introduction
Proposed Integration Methodology
Logic Synthesis
Defect/Fault Tolerance
Conclusions

## Slide 22: Defect/Fault Tolerance
Permanent Defect Tolerance
Testing Transient Fault Tolerance Performance
Transient Fault
Tolerance
Performance Optimization
Fabrication
Logic Synthesis

## Slide 23: Defect/Fault Tolerance
Permanent Faults occur mostly in fabrication and are tolerated in post-fabrication by redundancy and reconfigurability (mapping).
Transient Faults occur in field and are tolerated by redundancy

## Slide 24: Defect/Fault Tolerance
Defect tolerance is achieved by realizing a target logic function on a defective crossbar using row and column permutations
For the worst-case, N!M! permutations are required to find a successful mapping for NXM crossbar.
  Defect-unaware algorithms aim to find the largest possible kXk defect-free sub-crossbar from a defective NXN crossbar where k ≤ N;
  Defect-aware considers the defect characteristics (stuck-at-0 or stuck-at-1), then decide which switch to employ during the mapping.

## Slide 25: Defect/Fault Tolerance
Proposed method utilizes a sensitivity analysis of crossbar to specify critical switches, and strengthens them with mitigation factors

## Slide 26: Defect/Fault Tolerance
For each input, the simulation algorithm compares the given output with the correct one.
the number of defective outputs with a SA0 (resp., SA1)

## Slide 27: Defect/Fault Tolerance
For each input, the simulation algorithm compares the given output with the correct one.
the number of defective outputs with a SA0 (resp., SA1)
Lattice design
Sensitivity maps

## Slide 28: Defect/Fault Tolerance
For each input, the simulation algorithm compares the given output with the correct one.
the number of defective outputs with a SA0 (resp., SA1)
Sensitivity metrics:
  The average n° of defective outputs on sensitive cells
  The average n° of defective outputs on full lattice

## Slide 29: Defect/Fault Tolerance

## Slide 30: Defect/Fault Tolerance

## Slide 31: Defect/Fault Tolerance
SA1
SA0
Repair cells

## Slide 32: Defect/Fault Tolerance
Monte-Carlo test is costly
  Algebraic Analysis: using Inclusion Ratio and probabilistic fault
Transient faults are modelled as SA0 or SA1
Fault Tolerance: Redundancy
Enlarging the area:
Adding row or column
In optimal the area:
Switch redundancy
f = x1x2 + x2x3 + x3x4
f = x1x2x3+ x2x3 + x3x4

## Slide 33: Outline
Introduction
Proposed Integration Methodology
Logic Synthesis
Defect/Fault Tolerance
Conclusions

## Slide 34: Conclusions
Nano-switches are good alternatives to CMOS Boolean logic implementations
They are prone to defects and variability
Defect characterization and fault modeling are required for
  Reliable computation (fault mitigation)
  Area and power minimization under fault mitigation

## Slide 35: Integrated Synthesis Methodology for Crossbar Arrays
M. Ceylan Morgul, Luca Frontini, Onur Tunali, Elena Ioana Vatajelu,
Valentina Ciriani, Lorena Anghel, Csaba Andras Moritz, Mircea R. Stan,
Dan Alexandrescu, Mustafa Altun
This project has received funding from the European Union's H2020 research and innovation programme under the Marie Skłodowska-Curie grant agreement No 691178.
This work is supported by the TUBITAK-Career project #113E760