## Slide 1: Defect Tolerance in Diode, FET, and Four-Terminal Switch based Nano-Crossbar Arrays
IEEE/ACM International Symposium on Nanoscale Architectures, NANOARCH 2015
July 8th, 2015
Onur Tunalı & Mustafa Altun
Presenter: Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/
This work is supported by the TUBITAK-Career project #113E760

## Slide 2: Nano-Crossbar Arrays and Defects
Nano array and 3 different logic families
Defects are the main headache in nano arrays
Objective: Designing a fast heuristic algorithm for logic mapping on defective crossbars of 3 different logic families

## Slide 3: Defects in Diode based Nano Arrays
Ideally
f = A B + C D
Each crosspoint is either closed (diode connected) or open.
What if a crosspoint is closed when it is supposed to be open?
What if a crosspoint is open when it is supposed to be closed?
With a defect
f = A B + B C D
With a defect
f = A + C D
How to tolerate defects?

## Slide 4: Defects in FET based Nano Arrays
Ideally
f = (A B + C D)ꞌ
With a defect
f = 0
How to tolerate defects?
Each crosspoint is either closed (MOS or shorted) or open.
What if a crosspoint is closed when it is supposed to be open?

## Slide 5: Defects in Four-terminal Switch based Nano Arrays
Each crosspoint is either closed or open depending on the applied literal.
What if a crosspoint is always closed when it is supposed to switch?
What if a crosspoint is always open when it is supposed to switch?
Ideally
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
0
1
With a defect
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
With a defect
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
How to tolerate defects?

## Slide 6: Proposed Algorithm
Algorithm Steps:
Sort function and crossbar matrix
Obtain reduced matrix
Start subarray search
Compare sets of double indices, if equal sets found in 20,000 trials there is a matching otherwise not.
Key concepts:
Row and column permutations of matrix produce equivalent logic function.
Double index is (a, b) tuple which shows the number of same elements in a row and a column
Necessary and sufficent condition: If two matrices have the same set of double indices, then they are identical

## Slide 7: Experimental Results
For each benchmark function, 600 crossbars are generated. 600 is chosen due to stabilization of tolerance fluctuations.
It takes 0.2 seconds for each sample in average to check a valid mapping that satisfies an accuracy of 99% compared with an exhaustive search. This shows the effectiveness of our algorithm.

## Slide 8
THANK YOU!