## Slide 1: ELE 523E COMPUTATIONAL NANOELECTRONICS
W8: Faults Analysis and Tolerance, 29/11/2021
FALL 2021
Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: Outline
Definitions: defect, faults, errors, failures…
  Reliability versus quality
Faults in nanoscale
Fault models
  Stuck-at faults
  Transition faults
Fault and failure analysis
  Deterministic
  Probabilistic
Fault tolerance in nano-crossbar arrays
  Deterministic
  Fault and failure analysis
Transient fault tolerance

## Slide 3: Definitions
Defect: a physical problem
Fault: an abnormal condition or defect
Defect and faults ocur at the component, equipment, or sub-system level which may lead to a failure
Error: incorrect value or information in computing
Fault/Defect
Failure
0
1
Error

## Slide 4: Definitions
Latent Fault/Defect: not causing an error yet
Latent Error: not causing a failure yet
Latent Error
0
AND
0
1
0
Latent Defect
Latent Defect
Gate Oxide Breakdown
0
1
Don’t Care Condition

## Slide 5: Definitions
Permanent versus Temporary faults
Permanent versus Transient faults
Pre-field (Quality) versus In-field (Reliability) faults
Fault tolerance: there is fault, but no error
Error tolerance: there is error, but no failure
Quality
Faults happen before first usage
Post-fabrication fault analysis
Relatively easier to fix faults
  Detecting faults followed by reconfiguration or refabrication
Reliability
Faults happen any time in use
Transient probability analysis is needed
Harder to fix faults
  The only way is redundancy
  Dummy devices added

## Slide 6: Faults in Nanoelectronics
Faults are the main headache in nanoscale.
  Up to 20% fault ratio in fabrication processes
  Transient fault ratios are also high
  Faults are inevitable and must be handled
Faults in self-assembled nano arrays

## Slide 7: Fault Models
Model: a simplified and idealized understanding of physical systems
Models make easier to understand, define, quantify, visualize, or simulate faults
Limitations
  "All models are wrong, but some are useful "
  More failure mechanisms ⟼ less accurate models
  More fault types ⟼ more complex models, sometimes not realistic
8 different defects with 8 different models
How about model dependencies?

## Slide 8: Fault Models
Different components have different reliability predictions
Different components have different transient fault models

## Slide 9: Fault Models and Analysis
Stuck-at faults
  Stuck-at 1 and stuck-at 0
  Stuck-at ON and stuck-at OFF
  Stuck-at open and stuck-at shorted (bridging faults)
Transition faults
  Switching faults: 0-to-1 and 1-to-0
  Bit flips
Degradation based faults
Pre-field faults are analyzed/detected by certain deterministic tests
In-field faults are predicted with probability analysis

## Slide 10: Stuck-at 1 Fault Anaysis
0
0
AND
0
Fault/Error probability ϵ: a gate constantly evaluates logic 1 (stuck-at 1) with ϵ.
0
1
AND
0
1
0
AND
0
1
1
AND
1
Ideally
With a fault
0 with a probability of 1- ϵ
1 with a probability of ϵ
1 with a probability of 1

## Slide 11: Stuck-at 1 Fault Anaysis
0
0
0
Fault/Error probability ϵ: a gate constantly evaluates logic 1 (stuck-at 1) with ϵ.
0
1
1
1
0
1
1
1
1
Ideally
With a fault
0 with a probability of 1- ϵ
1 with a probability of ϵ
1 with a probability of 1
OR
OR
OR
OR

## Slide 12: Stuck-at 1 Fault Anaysis
Error/fault probability ϵ : independently each gate constantly evaluates logic 1 with ϵ.
Example:
What is the probability Px that the circuit produces an incorrect result.
a
b
c
x
AND
OR
Px = (1-c)ϵ + (c)(1-a)(1-b) (1-(1-ϵ)(1-ϵ))

## Slide 13: Stuck-at 1 Latent Fault Anaysis
Error/fault probability ϵ : each gate constantly evaluates logic 1 with ϵ.
Example:
What is the probability Pl that the circuit produces a correct result with a latent fault.
a
b
c
x
AND
OR
Pl = 1-Px-(1-ϵ)2

## Slide 14: Stuck-at 0 Fault Anaysis
0
0
AND
0
Fault/Error probability ϵ: a gate constantly evaluates logic 0 (stuck-at 0) with ϵ.
0
1
AND
0
1
0
AND
0
1
1
AND
1
Ideally
With a fault
0 with a probability of ϵ
1 with a probability of 1- ϵ
0 with a probability of 1

## Slide 15: Stuck-at 0 Fault Anaysis
0
0
0
Fault/Error probability ϵ: a gate constantly evaluates logic 0 (stuck-at 0) with ϵ.
0
1
1
1
0
1
1
1
1
Ideally
With a fault
0 with a probability of ϵ
1 with a probability of 1- ϵ
0 with a probability of 1
OR
OR
OR
OR

## Slide 16: Stuck-at 0 Fault Anaysis
Error/fault probability ϵ : each gate constantly evaluates logic 0 with ϵ.
Example:
What is the probability Px that the circuit produces an incorrect result.
a
b
c
x
AND
OR
Px = (c)(1-(1-a)(1-b)) (1-(1-ϵ)(1-ϵ))

## Slide 17: Stuck-at 0 Latent Fault Anaysis
Error/fault probability ϵ : each gate constantly evaluates logic 0 with ϵ.
Example:
What is the probability Pl that the circuit produces a correct result with a latent fault.
a
b
c
x
AND
OR
Pl = 1-Px-(1-ϵ)2

## Slide 18: Transition Fault Analysis
0
0
AND
0
Error/fault probability ϵ : a gate evaluates the incorrect result, the complement of the correct Boolean value, with ϵ.
0
1
AND
0
1
0
AND
0
1
1
AND
1
Ideally
With a fault
0 with a probability of 1- ϵ
1 with a probability of ϵ
1 with a probability of 1- ϵ
0 with a probability of ϵ

## Slide 19: Transition Fault Analysis
0
0
0
Error/fault probability ϵ : a gate evaluates the incorrect result, the complement of the correct Boolean value, with ϵ.
0
1
1
1
0
1
1
1
1
Ideally
With a fault
0 with a probability of ϵ
1 with a probability of 1- ϵ
0 with a probability of 1- ϵ
1 with a probability of ϵ
OR
OR
OR
OR

## Slide 20: Transition Fault Analysis
Error/fault probability ϵ : each gate evaluates the incorrect result, the complement of the correct Boolean value, with ϵ.
Example:
What is the probability Px that the circuit produces an incorrect result.
a
b
c
x
AND
OR
Px = ϵ - (2ϵ2- ϵ)c

## Slide 21: Transition Fault Analysis
Error/fault probability ϵ : each gate evaluates the incorrect result, the complement of the correct Boolean value, with ϵ.
Example:
What is the probability Py that the circuit produces an incorrect result.
a
c
b
c
y
AND
AND
OR
Py = 3ϵ - 5ϵ2 + 2ϵ3- (ϵ - 2ϵ2)(a+b)c + (2ϵ2 - 4ϵ3)abc

## Slide 22: Transition Fault Analysis
Px = ϵ - (2ϵ2- ϵ)c
Py = 3ϵ - 5ϵ2 + 2ϵ3- (ϵ - 2ϵ2)(a+b)c + (2ϵ2 - 4ϵ3)abc
Both circuits, A and B, implement the same Boolean function (a+b)c.
Which circuit is better in fault tolerance?
A
B

## Slide 23: Faults in Nano-Crossbar Arrays
Ideally
f = A B + C D
Each crosspoint is either closed (diode connected) or open.
What if a crosspoint is closed when it is supposed to be open?
What if a crosspoint is open when it is supposed to be closed?
With a fault
f = A B + B C D
With a fault
f = A + C D
How to tolerate faults?

## Slide 24: Faults in Nano-Crossbar Arrays
Ideally
f = (A B + C D)ꞌ
With a fault
f = 0
How to tolerate faults?
Each crosspoint is either closed (FET or shorted) or open.
What if a crosspoint is closed when it is supposed to be open?

## Slide 25: Faults in Nano-Crossbar Arrays
Each crosspoint is either closed or open depending on the applied literal.
What if a crosspoint is always closed when it is supposed to switch?
What if a crosspoint is always open when it is supposed to switch?
Ideally
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
0
1
With a fault
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
With a fault
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
How to tolerate faults?

## Slide 26: Fault Tolerance Stages
Stages: Fabrication
Stakeholder: Chip Manufacturer
Application Designer
Post-fabrication
In-field/ Service
End User
Mitigation Methods- Adding Redundancy: Error-correcting codes, TMR, NAND demultiplexing
Fabrication, verification and test
Permanent Faults
Permanent+
Transient Faults
Mitigation Methods: Configuring around defects
Mitigation Methods: Self-testing, reconfiguring
Test and verification
Design
Final Product
Nanomaterials: carbon nanotube, nanowires

## Slide 27: Post-fabrication and Defects
Nano-array fabricated with bottom-up methods
In post-fabrication, the ciruit is configured

## Slide 28: Configuration of a circuit
A logic function is implemented with configuration
A full-adder with activating and deactivating the switches
Activated
Deactivated

## Slide 29: Configuration of a circuit
In a defect-free array, straitghtforward process
A B C A B C
A B
B C
A C
A B C
Input Lines
Output Lines
Activated switch
Deactivated switch
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6
F = A B + B C + A C + A B C
(1) Given function
(2) Realized function
F = A B + B C + A C + A B C
Mapping

## Slide 30: Defects
Stuck-at deactivated, switch cannot be activated
Stuck-at activated, switch cannot be deactivated
: Stuck-at deactivated switch
: Stuck-at activated switch
: Configurable switch
: Defective switch

## Slide 31: Mapping with Defects
In a defective array, every mapping is not valid
Activated switch
Deactivated switch
Mapping
A B C A B C
(2) Realized function
A B
A B C
A C
A B C
C
F’ = A B + A B C + A C + A B C + C
Input Lines
Output Lines
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6
(1) Given function
F = A B + B C + A C + A B C
F’
F

## Slide 32: Defect-aware mapping
Mapping is performed with employing defects
B A C A B C
(2) Realized function
A B
B C
A C
A B C
Input Lines
Output Lines
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6
(1) Given function
F = A B + B C + A C + A B C
F = A B + B C + A C + A B C
Activated switch
Deactivated switch
Mapping
A B C A B C
A B
A B C
A C
A B C
C
Previous mapping
F’
F

## Slide 33: Defect-unaware mapping
First, a defect-free sub-array is found
Input Lines
Output Lines
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6 I7
(1) Given function
F = A B + B C + A C + A B C
Defect-free sub-aray
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6 I7
I7 and O5
discarded I7

## Slide 34: Defect-unaware mapping
Second, configuration is starightforward
Input Lines
Output Lines
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6 I7
F = A B + B C + A C + A B C
(1) Given function
Mapping
A B C A B C
A B
B C
A C
A B C
(2) Realized function
F’ = A B + B C + A C + A B C
F’
F

## Slide 35: In-field Transient Faults
Transient faults occur according to a time-domain
They are predicted with probability analysis
Diode and FET Components show different behaviour regarding to the fault type
  Stuck-at OFF: switch is not capable of conducting current, infinite resistance
  Stuck-at ON: switch is constantly conducting current, zero resistance
Diode
Stuck-at OFF only switch
Stuck-at ON entire output line
FET
Stuck-at OFF entire output line
Stuck-at ON only switch

## Slide 36: Diode-based Nanoarray
Stuck-at OFF, no connection between terminals
  Only faulty switch is affected
Stuck-at ON, terminals always connected
  Entire line is affected
: Stuck-at OFF switch
: Stuck-at ON switch
: Functional switch
: Unusable switch
Terminals
Vdd
Gnd

## Slide 37: FET-based Nanoarray
Stuck-at OFF, no connection between terminals
  Entire line is affected
Stuck-at ON, terminals always connected
  Only faulty switch is affected
: Stuck-at OFF switch
: Stuck-at ON switch
: Functional switch
: Unusable switch

## Slide 38: Transient Fault Tolerance
Stochastic computing
Randomly shuffled N number of inputs and outputs
Values are calculated as the number of 1 valued input/output lines over N
Parallel operation
Von Neumann’s multiplexing unit, 1956
Values are calculated as the number of 1 valued input/output lines over N
Serial operation

## Slide 39: Multiplexing for Transition Faults
Error probability ϵ : a gate evaluates the incorrect result, the complement of the correct Boolean value, with ϵ.
Calculate z with and without error
ϵ ⟶ ϵ(1-2z)

## Slide 40: Multiplexing for Stuck-at 1 Faults
Calculate z with and without error
ϵ ⟶ ϵ(1-z)
Error/fault probability ϵ : each gate constantly evaluates logic 1 with ϵ.

## Slide 41: Multiplexing for Stuck-at 0 Faults
Calculate z with and without error
ϵ ⟶ ϵ(z)
Error/fault probability ϵ : each gate constantly evaluates logic 0 with ϵ.

## Slide 42: Transient Fault Tolerance
Triple modular redundancy (TMR)
Increase area 2 times plus an XOR gate
For only detection
Dual modular redundancy (DMR)
Increase area 3 times plus XOR gates
For both detection and correction
For only a single output fault
For only a single output fault

## Slide 43: Transient Fault Tolerance
Satisfying Hamming distance
Applicable for large circuits
For only detection
Extra parity bit
For both detection and correction
For only odd number of output faults
Practical for large circuits
For multiple output faults

## Slide 44: Suggested Readings
Moore, E. F., & Shannon, C. E. (1956). Reliable circuits using less reliable relays. Journal of the Franklin Institute, 262(3), 191-208.
Von Neumann, J. (1956). Probabilistic logics and the synthesis of reliable organisms from unreliable components. Automata studies, 34, 43-98.
Han, J., Taylor, E., Gao, J., & Fortes, J. (2005, July). Faults, error bounds and reliability of nanoelectronic circuits. In 2005 IEEE International Conference on Application-Specific Systems, Architecture Processors (ASAP'05) (pp. 247-253). IEEE.
DeHon, A. (2003). Array-based architecture for FET-based, nanoscale electronics. Nanotechnology, IEEE Transactions on, 2(1), 23-32.
Han, J., & Jonker, P. (2003). A defect and fault-tolerant architecture for nanocomputers. Nanotechnology, 14(2), 224.
Rao, W., Orailoglu, A., & Karri, R. (2007, April). Logic level fault tolerance approaches targeting nanoelectronics plas. In 2007 Design, Automation & Test in Europe Conference & Exhibition (pp. 1-5). IEEE.
Tunali, O., & Altun, M. (2016) Permanent and Transient Fault Tolerance for Reconfigurable Nano-Crossbar Arrays. IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems.