## Slide 1: ELE 523E COMPUTATIONAL NANOELECTRONICS
W6: Probabilistic and Approximate Computing, 8/11/2021
FALL 2021
Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: Outline
Overview of probabilistic computing
  Strengths
  Weaknesses
  Application areas
Stochastic computing with logic gates
  Circuit analysis
  Synthesis of stochastic inputs
  Synthesis of polynomial functions
Probabilistic switches
Approximate computing
  Software level
    Appling probabilistic or heuristic methods
    Skipping tasks
    Memoization
  Hardware level
    Voltage and size scaling
    Inexact structures

## Slide 3: Probabilistic Computing
Deterministic
Subsequent state of the system is determined deterministically
Probabilistic
Subsequent state of the system is determined probabilistically
Deterministic
Deterministic
Deterministic
Probabilistic

## Slide 4: Why Probabilistic Computing?
Strengths
  Easier to implement arithmetic operations.
  Works efficiently in encoding/decoding
  High degree of transient error tolerance.
  Exploit randomness that is a fact in nanoscale.
  Used in modeling probabilistic behavior of nanotechnologies.
Weaknesses
  Accuracy problems.
  Long computational times.

## Slide 5: Stochastic Computing
Stochastic computing (SC) is a probability computing that depends on random bit streams.
0,1,0,1,1,0,1,0
Random Bit Streams
P(x=1) = 4/8
x
0,1,0,0,0,1,0,0
P(y=1) = 2/8
y
Stochastic Computing
x=4/8
y=2/8
z
AND

## Slide 6: Random Bit Streams
Randomly assigning each bit value
CONVENTIONAL
The stream probability p represents the probability of having 1 for each bit
The stream has a binomial distribution in terms of the number of 1s
Less accurate
Perfectly random
Randomly shuffling a bit stream
The stream probability p represents (total number of 1s)/(total number of bits)
The stream has a deterministic behaviour in terms of number of 1s
More accurate
The longer the streams the closer these methods.

## Slide 7: Stochastic Computing
Stochastic circuit
Probabilistic
Probabilistic
Deterministic
p1=2/6, p2=2/6, p3=2/6, p4=1/6, p5=5/6, p6=2/6

## Slide 8: Accuracy of SC
x=4/8
y=2/8
z
AND
0,1,0,0,0,1,0,0
0,1,0,1,1,0,1,0
0,1,0,0,1,0,0,0
0,1,0,1,1,0,1,0
z=1/8
z=2/8
1,0,0,0,0,1,0,0
0,1,0,1,1,0,1,0
z=0/8
Which one is right?

## Slide 9: Accuracy of SC
x=4/8
x=4/8
z
AND
0,1,0,1,1,0,1,0
z=4/8
Dependency is important!
0,1,0,1,1,0,1,0
0,1,0,1,1,0,1,0
Conventionally, input streams are independent

## Slide 10: Accuracy of SC
Randomly assigning each bit value
CONVENTIONAL
The stream probability p represents the probability of having 1 for each bit
The stream has a binomial distribution
Randomly shuffling a bit stream
The stream probability p represents (total number of 1s)/(total number of bits)
Calculate the error as
Calculate the error rate?
AND

## Slide 11: Randomly Assigning
x=2/4
y=2/4
AND
Example:
Consider 4-bit input bit streams x and y such that each bit is 1 with an independent probability of p=1/2.
Find the probability of accurate computation z=1/4.
Find the probability of having z=0/4.
Find the probability of having z=2/4.
Find the probability of having z=3/4.
Find the probability of having z=4/4.
Find the everage error rate.
z

## Slide 12: Randomly Shuffling
x=2/4
y=2/4
AND
Example:
Consider randomly distributed 4-bit input bit streams x and y such that half of its bits are 1 and the other half 0.
Find the probability of accurate computation z=1/4.
Find the probability of having z=0/4.
Find the probability of having z=2/4.
Find the probability of having z=3/4.
Find the probability of having z=4/4.
Find the everage error rate.
z

## Slide 13: Improving the Accuracy
Using correlated bit streams
Using quasi-random bit streams
Low-discrepancy vs. random sequence
Error-free computing
1 gate vs. 1000 gates doing the same job

## Slide 14: Defect Tolerance in SC
x=4/8=(0.100)2
y=2/8=(0.010)2
AND
What if there is a bit-flip in an input?
z=1/8=(0.001)2
0,1,0,0,0,1,0,0
0,1,0,1,1,0,1,0
z=1/8
(0.100)2 x (0.010)2 = (0.001)2

## Slide 15: Performance of Randomness
Ingredients of “Çiğ Köfte”
Kneading “Çiğ Köfte”
Ready to serve “Çiğ Köfte”
The longer the kneading time the tastier the “Çiğ Köfte”.
The longer the kneading time the more homogeneous (accurate) the “Çiğ Köfte”.
Heterogeneous to Homogeneous: HOW?

## Slide 16: Performance of SC
The longer the bit streams the more accurate the computation.
The longer the bit streams the more reliable the computation.
The longer the bit streams the slower the computation.
0,1,0,1,1,0,1,0,…..
Bit Streams

## Slide 17: Arithmetic Operations with SC
Multiplication: : x x y = z
AND
3-bit deterministic multiplier (30 gates)
3-bit stochastic multiplier (1 gate)
x=(0.100)2
y=(0.100)2
z=(0.010)2
At least how many bits shoud a stream have?
At least how many stream bits for an n-bit multiplier?

## Slide 18: Arithmetic Operations with SC
Scaled addition: : x(s) + y(1-s) = z
x
y
s
z
MUX
1,1,1,1,1,0,1,1
0,0,1,0,0,1,1,0
1,0,0,1,0,1,0,1
1,0,1,1,0,0,1,1
MUX
x=7/8, y=3/8, s=4/8, z=5/8
1
0
1
0

## Slide 19: Arithmetic Operations with SC
Example:
Find the expression of z for both stochastic and deterministic inputs applied.
x1
x2
x3
x4
z
1
0
AND
MUX
NOT

## Slide 20: Synthesis Problem-1
Problem: How to construct a logic circuit in order to implement given output probabilities with a set of input probabilities?
P(x = 1) = 0.4
P(z = 1) = 0.6
1,0,1,1,0,1,0,0,0,0
0,1,0,0,1,0,1,1,1,1
P(z = 1) = P(x = 0)
P(x = 1) = 0.4
P(z = 1) = 0.2
0,1,0,1,0,0,1,1,0,0
0,0,0,1,0,0,1,0,0,0
P(z = 1) = P(x = 1) P(y = 1)
1,0,1,1,0,0,1,0,0,1
P(y = 1) = 0.5
P(x = 1) = 0.4
P(z = 1) = 0.3
0,0,1,0,1,0,1,0,1,0
0,1,0,0,0,1,0,0,0,1
P(z = 1) = P(x = 0) P(y = 0)
1,0,0,1,1,0,0,1,1,0
P(y = 1) = 0.5
Example:
Implement output probabilities 0.6, 0.2, and 0.3 with using input probabilities of 0.4 and 0.5.

## Slide 21: Synthesis Problem-1
Theorem (Qian et al. 2011): With input probabilities = {0.4, 0.5}, we can synthesize arbitrary decimal output probabilities.
Example: Synthesize q = 0.757
(Black dots are inverters)

## Slide 22: Synthesis Problem-2
Problem: How to construct a logic circuit in order to implement a polynomial g(t) where both t and g(t) are in unit interval?

## Slide 23: Synthesis Problem-2
Example:
Implement g(t) = 3/8 t2 + 5/8 t.
AND
MUX
1
0
t
t
3/8
t
g(t)

## Slide 24: Synthesis Problem-2
Example:
Implement g(t) = t3 – 2t2 + 1.
NOR
MUX
1
0
t
t
t
1
g(t)

## Slide 25: Synthesis Problem-2
Example:
Implement g(t) = 9/4 t2 – 15/8 t + 5/8 and test on g(1/2).
t
t
5/8
g(t)
t
MUX
0
1
2
3
0
1/8
1

## Slide 26: Synthesis Problem-2
Theorem (Qian et al. 2012): With using Bernstein polynomials, we can synthesize any polynomial g(t).
g(t) = 9/4 t2 – 15/8 t + 5/8
= 5/8 B0 + 0 B1 + 1/8 B2 + 1 B3
Bi = probability that the output of the adding unit is i.
B0 = (1-t)3
B1 = 3 t(1-t)2
B2 = 3 t2(1-t)
B3 = t3
Example:
Implement g(t) = 9/4 t2 – 15/8 t + 5/8.

## Slide 27: Probabilistic Two-Terminal Switch
0,1,0,1,1,0,1,0
P(x=1) = p = 4/8
x
A probabilistic switch is ON with a probability of p.
Can be implemented with stochastic bit streams.
Can be used to model probabilistic phenomena in nanoscale such as random defects.

## Slide 28: Probabilistic Two-Terminal Switch
A probabilistic MOS is a probabilistic switch.
* Probabilistic CMOS technology: A survey and future directions

## Slide 29: Probabilistic Two-Terminal Switch

## Slide 30: Synthesis Problem
Problem: How to construct a circuit in order to implement a given binary decimal numbers using p-switches with p=1/2 ?
Example:
Implement the output probabilities 0.112 and 0.0112 with p-switches with p=1/2.
0.0112
0.112

## Slide 31: Synthesis Problem
Progressing from the least-significant to the most-significant bits
Example:
Implement the output probability 0.10112 with p-switches with p=1/2.

## Slide 32: Synthesis Problem
Binary tree showing how to generate all possible switching circuits
(Wilhelm et al. 2008)

## Slide 33: Why Approximate?
Benefits
  Power saving
  Energy saving
  Time saving
  Area saving
At the cost of accuracy
Parallel Processing
Serial Processing
Power?
Energy?
Time?
Area?

## Slide 34: Why Approximate?
Applications
  Problems not having a unique solution
  Solution space is large
  Video, audio, and image applications not requiring perfect accuracy
Scheduling the exam week with exam dates and hours
Synthesizing a circuit with gates doing a certain task
Finding a logic truth table of a certain task
Image processing
Calculator

## Slide 35: Software Level Approximation
Genetic/evolutionary and heuristic algorithms
Distrubution of random input assignements
Solution Space

## Slide 36: Software Level Approximation
Genetic/evolutionary and heuristic algorithms

## Slide 37: Software Level Approximation
Memoization: remembering the past, use for the future
Our brains use it all the time. How about accuracy?
Suitable for applications having small variances.
Low variance

## Slide 38: Hardware Level Approximation
* Probabilistic CMOS technology: A survey and future directions
Voltage scaling
Ideally zero variance; decreasing Vdd results in a variance increase

## Slide 39: Hardware Level Approximation
Approximate circuits are achieved by changing truth tables or target Boolean functions.
Exact adder (14 Gates)
App. adder (11 Gates)

## Slide 40: App. Adders for Image Processing
Noise
Matrix
Mean filter with Approximate adders

## Slide 41: App. Adders for Image Processing
New value= (11+111+222+220+222+111+11+111+222)/9=134
Mean filter

## Slide 42: Approximate 1-bit Full Adders
Accurate Adder
Approximate 1
Approximate 2
Approximate 3
Approximate 4

## Slide 43: Approximate 1-bit Full Adders
IMPACT: imprecise adders for low-power approximate computing

## Slide 44: Approximate Ripple Carry Adders
Least significant
Most significant
Which full adders are approximate?
How to calculate an average error?

## Slide 45: Approximate Multiplier

## Slide 46: Approximate Multiplier
Costs

## Slide 47: Application of Approximate Multiplier
Power Save=40%
Power Save=60%
Power Save=90%

## Slide 48: App. Computing in Machine Learning
Neural Network:
Simple NN Structure

## Slide 49: Suggested Readings
Qian, W., & Riedel, M. D. (2008, June). The synthesis of robust polynomial arithmetic with stochastic logic. In Design Automation Conference, 2008. DAC 2008. 45th ACM/IEEE (pp. 648-653). IEEE.
Alaghi, A., & Hayes, J. P. (2013). Survey of stochastic computing. ACM Transactions on Embedded Computing Systems (TECS), 12(2s), 92.
Vahapoglu, E., & Altun, M. (2016, July). Accurate Synthesis of Arithmetic Operations with Stochastic Logic. In VLSI (ISVLSI), 2016 IEEE Computer Society Annual Symposium on (pp. 415-420). IEEE.
Wilhelm, D., & Bruck, J. (2008, July). Stochastic switching circuit synthesis. In Information Theory, 2008. ISIT 2008. IEEE International Symposium on(pp. 1388-1392). IEEE.
Moore, E. F., & Shannon, C. E. (1956). Reliable circuits using less reliable relays. Journal of the Franklin Institute, 262(3), 191-208.
Mittal, S. (2016). A survey of techniques for approximate computing. ACM Computing Surveys (CSUR), 48(4), 62.